Micro Tacho Tachometer Turnigy

Features:
To measure 2-9 Propeller and EDF units.
The maximum value 99999ot. / S

Features:
- Ultra sharp backlit LCD display
- 220mAh Lion battery included
- Compact and portable
- Automatic power off. (prevents battery discharge)
_ Weighing only 39 grams

Instructions for use:
Hold the power button for more than one second to switch on the device.
Press the SET button to select the number of blades on your measured propeller or EDF.
Aim the tachometer directly on the rotating propeller blades measured from a distance of about 10 cm.
LCD display will show the rotational speed in real time (rev / s) and after the measurement remains displayed maximum value.
To have a backlit display, hold the SET -3 seconds longer.
Take measurements with good lighting and avoid fluorescent lighting because they can cause incorrect measurements / reading /.

Warning!
Always measure at a safe distance from rotating objects. Never stand in front or beside the rotating propeller. When using this equipment, always wear safety glasses.

Translated by: OwlCastle
more at: http://www.wwii-rcmodely.mypage.cz/