Global null$, header$
null$ = chr$(0)
header$ = chr$(85) + chr$(0) + chr$(11) + chr$(0)
Attempt$="Attempting to connect........"
Connect$="Connected"
NotConnect$="Not connected"

Graphics On
Orientation 2
SetScale 480, 854
TextSize 40
Color 50,50,50
TextColor 100,100,100

'SETUP THE SCREEN
'button position variables
	dim px(4)=0,240,240,240,240
	dim py(4)=0,100,300,500,700
	
'draw buttons as red circles
CLS
color 100,0,0
For c= 1 to 4
	Circle  px(c),py(c),20,1
Next c
color 50,50,50

'Set channel values at midpoint on startup, but not after lost connection, so do it here
	ch1=50
	ch2=50
	ch3=50
	ch4=50

'               ****** MAIN LOOPS ******
do

  Drawtext Attempt$, 430,50,90,1
  wait 100
  TcpOpen 1, "10.10.100.254", 8899, "c", 12000, 1000

    if TcpGetState(1) = 1 then

	Drawtext Connect$,360,50,90,1
      	wait 1000

	do while TcpGetState(1) = 1

		'Main Loop....check for screen touch, update and keep sending channel values

		Touch x,y,10  ' This is milliseconds. If screen not touched, x and y are both -1

			If y<200 and y>-1 then
				px(1)=x
				ch1= Int(x/4.8)
			ElseIf y>200 and y<400 then
				px(2)=x
				ch2= Int(x/4.8)
			ElseIf y>400 and y<600 then
				px(3)=x
				ch3= Int(x/4.8)
			ElseIf y>600 and y<800 then
				px(4)=x
				ch4= Int(x/4.8)
			Endif

		'draw new button positions	 and get rid of messages, if any
			CLS
			color 100,0,0
			For c= 1 to 4
				Circle  px(c),py(c),20,1 
			Next c
			color 50,50,50
			sendRawChannels(ch1, ch2, ch3, ch4)
	loop
   endif

  Drawtext NotConnect$,300,50,90,1
  SetClipboard TcpGetError$(1)  'store the error message on the clipboard
  wait 1
  TcpClose 1

loop
end

Sub sendRawChannels(ch1, ch2, ch3, ch4)
  ' Add header
  packet$ = header$

  ' Add channel values
  packet$ = packet$ + chr$(ch1 & 255)  
  packet$ = packet$ + chr$(ch2 & 255)  
  packet$ = packet$ + chr$(ch3 & 255)  
  packet$ = packet$ + chr$(ch4 & 255)  

  ' Two bytes not used
  packet$ = packet$ + null$  
  packet$ = packet$ + null$  

  sum = 0
  for i = 1 to 10
    sum = sum + ascii(mid$(packet$, i, 1))
  next

  ' Add checksum byte
  packet$ = packet$ + chr$(sum % 256)

  TcpWrite 1, packet$

End Sub