Translated by or levy

ESC Program with the transmitter (4 Steps)

1. Enter the programming mode
2. Select the items programmable
3. Set the value of the item (programmable value)
4. Exit the programming mode

1 - Enter the programming mode:

Connect the transmitter with the throttle up, fast position, connect the battery esc.

Wait 2 seconds, the engine must issue special tone like "beep-beep"

Wait 5 seconds, special tone like "56712" shall be issued, which means program mode is entered.

2 - Select the programmable items.

After entering the programming mode, you can listen to eight tones in a loop in the following sequence. If you move the throttle stick to bottom within 3 seconds after one kind of tones, then this item is selected

1. "Beep" brake (one short tone)
2. "beep - beep) type of battery (two short tones)
3. "beep - beep - beep) mode cutoff (3 short tone)
4. "beep - beep - beep - beep) cutoff (4 short tones)
5. "Beep ......" boot mode (one long tone)


Note: 1 long beep ...... "" = 5 "beep". short

3. Set the value of the item (programmable value)

you will ouvur loop in various tones. Set the value corresponding to a tone by moving throttle stick up when you hear the tone, then a special tone "1515" emits, means that the value is set and saved. (Keep the throttle stick in the top position, you will return to step 2 and select another iten.
Moving the stick to bottom within 2 seconds, you will exit the program directly.


4. Exit the programming mode

1 - In step 3, after special tone "1515" throttle move down within 2 seconds

2 - In step 2, after the tone, "......" beep beep ...... (That is, item # 8) to move the throttle stick to bottom within 3 seconds