Turnigy TrackStar Waterproof 1/10 Brushless ESC

Note: For proper ESC operation, please adjust transmitter as follows

Set High EPA or ATV to maximum setting; max throttle

Set Low EPA or ATV to maximum setting; max brake

Set throttle trim in the middle position

Set throttle Exponential to Zero.

Set Throttle mode F50/B50 for Practice Mode.

Set Throttle mode F70/B30 for Racing Mode.

Transmitter Calibration:

Press and hold the push button and then turn on ESC switch - Orange LED on

Pull to Full Throttle – Orange LED flashing and then solid on.

Push to Full Brake – Blue LED flashing and then solid on.

Neutral – Orange & Blue LED flashing, and then on,about 2sce All LED solid Off.

Switch Power off, then turn on again, the ESC be ready to work.

Normal Operation:

Orange and Blue LED on for Forward with pause then Reverse

Blue on for  Forward Only

As Battery voltage get to warning point, Blue LED blink.

As temperature voltage get to warning point, Orange LED blink.